## Slide 1: Non-pairwise Collision
Yuhong Zhang
August 7, 2015

## Slide 2: Physics Requirement of Non-Pairwise
Non-pairwise
In a nominal collider design, one bunch of a beam usually collides with only one bunch or a small set of bunches of the other beam (depending on number of IPs and ratio of circumference of the two rings)
For MEIC, due to requirement of polarization measurement of a beam with high bunch repetition rate (and unable to do bunch-by-bunch measurement), ideally
    (strong case) any bunch of the electron beam should collide with every bunch in the ion beam, and vis verse, any bunch of the ion beam will collide with every bunch in the electron beam
    (weak case) any even bunch of the electron beam should collider with every even bunch in the ion beam, similarly, any odd bunch of the electron beam will collide with every odd bunch in the ion beam
Realization
Two collider rings must have different numbers of bunches (harmonic numbers);
For the strong case, the difference must be an ODD number (eg: 3416 vs. 3417);
For the weak case, the difference must be an EVEN number (eg. 3416 vs. 3418)
The ring circumferences will be different too

## Slide 3: Some Basic Facts
Two IP complication
Asymmetric: unequal number of bunches in two half rings
unequal distances from IP to IP in the ring
(example: electron ring 1708 and 1708, ion ring 1708 and 1710
electron ring 1708 and 1708, ion ring 1708 and 1709)
Gear-Change
Increment of bunches in the ion ring must be an even number (+2, +4, +6, +8, etc.) in order to maintain an ODD number difference of bunch numbers
Location of the 2nd IP will shift a very small distance
(example: if +2, left ring 1708+1, right ring 1709+1, IP moves 0.04 cm
if +4, left ring 1708+2, right ring 1709+1, IP movers 0.08 cm)
However, it can be eliminated by adjusting the path length

## Slide 4: Asymmetric Ring Design
IP1
IP2
1709
+1,+2,+3
1708
1708
1708
+1,+2,+3

## Slide 5: Change of Harmonic Number (# of Bunches)
Ion kinetic energy | Harmonic number | Bunches in the left half ring | Bunches in the right half ring | Length of the left half ring | Length of the right half ring | Path length adjust
GeV |  |  |  | m | m | cm
51 | 3417 | 1708 | 1709 | 1075.92 | 1076.55 | 
22.326 | 3419 | 1709 | 1710 | 1075.92 | 1075.55 | 0.04
17.245 | 3421 | 1710 | 1711 | 1075.92 | 1076.55 | 0.11
14.23 | 3423 | 1711 | 1712 | 1075.92 | 1076.55 | 0.1
12.345 | 3425 | 1712 | 1713 | 1075.92 | 1075.55 | 0.14

## Slide 6: Some Comments
It is possible to arrange non-pairwise collision scenario, however it would be more complicated with two IPs
If both rings have even number of bunches, then it will enable half bunches of one ring collide with half bunches of another ring; the other two sets of half bunches will collide themselves.
Loss of symmetry (between the left and right half ring) is a concern.
Gaps will travel along the bunch train, it doubles the loss of luminosity