## Slide 1: Longitudinal Single-Bunch Instability in JLEIC Design
Rui Li
(2/18/16)

## Slide 2: Outline
Introduction
Collective interaction of a bunch via wakefield or impedance
Longitudinal single-bunch Instability
Threshold in JLEIC designs
Summary

## Slide 3: 1. Introduction
  External magnetic or RF fields determine single particle dynamics for the design optics
  High intensity bunches could interact with itself via direct EM field interaction or via boundary conditions of vacuum pipe
  These collective interaction could cause the beam to undergo longitudinal or transverse instabilities
  There are many types of coherent instabilities.
  Bunch-induced fields with wavelengths short compared to bunch length may induce microwave instability in a single bunch.
  Longitudinal single bunch instability is one of the most early discovered instabilities, and has been well studied by theory, simulation and experiments.

## Slide 4
This instability could cause potential-well distortion, longitudinal microwave instability or turbulent bunch lengthening
It is not a fatal instability---not causing beam loss, but it causes bunch lengthening and increase of momentum spread.
At JLEIC, we are mostly safe from this instability. However, because of the wide energy range, ion species, and the electron cooling during collision, we should be cautious of the possibility of encountering this instability
Space charge at low energy in the booster ring may cause concern.

## Slide 5: Example Observation of Longitudinal Single-Bunch Instabilities
Observation at PSR
of Los Alamos

## Slide 6: Increase of Energy Spread
Y.-C. Chae et al, “Measurement of the longitudinal microwave instability in
the APS storage ring,” (2001)

## Slide 7: 2. Bunch Collective Interaction
Charged particles are guided, focused and accelerated by external dipole, quadruple magnetic field and RF fields
Each charged particle in a beam carries with it the self EM fields, which could be scattered or diffracted by vacuum pipe boundaries
The particles experience collective fields by direct interaction via space charge or CSR, or by indirect interaction via the image charge generated fields
Wakefield following a point
charge in a cylindrical pipe
with resistive wall (K. Bane)

## Slide 8: Field from a bunch traversed a cavity structure

## Slide 9: Impedance Generating Elements
RF cavities
Resistive walls
Shielded bellows
Unshielded bellows
Tapers
Flanges
BPMs
Pumping slots
Vacuum valves
Injection kickers
Abort kickers
Strip line kicker
(feedback system)
Clearing electrodes
Space charge
CSR
Collimators
Interaction region
We need to develop impedance budget by assessing impedance
from all such elements in JELIC beamlines

## Slide 10: Typical Impedance Behavior
Cause coupled bunch
instability
Cause single bunch
instability

## Slide 11: Example of LHC broad-band impedance budget

## Slide 12: Collective Instabilities
Linac
Recirculating
Accelerator or ERL
Storage
ring
Transverse
Longitudinal
Machine
Type
Beam
dynamics
Collective
Interaction
Single
bunch
Multi
bunch
Synchro
-betatron
Two
stream
coherent
incoherent
Coherence

## Slide 13: 3. Single-bunch Longitudinal Instability
Potential well distortion
Incoherent & coherent synchrotron tune shift
Longitudinal microwave instability

## Slide 14: Single Particle Longitudinal Dynamics
Equation of motion
Hamiltonian
Unperturbed stationary distribution for bunched electron beam
Solution of Haissinski equation (with quantum excitation due to SR)
What about equilibrium for ion beam under ecooling?

## Slide 15: Potential Well Distortion
The RF field generates a potential well for the particles
The wakefield of beamline cause distortion of the potential well modifies the incoherent synchrotron motion
The wakefield of the bunch is determined by the bunch length or the bunch longitudinal distribution
The potential well in turn determines the synchrotron tune shift and stationary bunch distribution in self-consistent way
Above transition, a inductive impedance will cause bunch lengthening
Potential well deformation is an incoherent effect
Hassinski
Solution
for e-beam
equilibrium

## Slide 16: Experimental Observation of Bunch Lengthening
Measurement
Simulation
(Y. Cai, SLAC-PUB-13570)
KEKB: L= 96nH (LER) and L=104nH (HER)
Wake model:
LER
HER

## Slide 17: Phase Space Ellipse Distortion for Electron or Proton Beams

## Slide 18: Longitudinal Microwave Instability (LMWI)
Density perturbation may occur on top
of stationary distribution
System responds to the perturbation
through wakefield or impedance
This could combine with slip factor
to cause microwave instability
Negative mass instability is space charge
caused by LMWI above transition

## Slide 19: LMWI for a Coasting Beam (zero energy spread)
-CSR,LSC
-resistive wall
-RF cavity,etc
Phase space
continuity
Dispersion relation

## Slide 21: LMWI for a Coasting Beam (finite energy spread)
Energy spread cause decoherence
or Landau damping
Stability Diagram
Threshold of LMWI
or

## Slide 22: LMWI for a Bunched Beam
Modes in longitudinal phase space
Mode mixing
Note:

## Slide 23: 4. Estimation of LMWI for JLEIC
General formula and its parametric dependence
LMBI threshold for PEP-II LER and JLEIC e-ring
LMBI threshold for RHIC and JLEIC ion rings

## Slide 24: LMBI Impedance Threshold and Parametric Dependences
LMWI threshold
Acceleration:
RF rebucketing, IBS, cooling:
Bunch splitting:
Machine impedance:

## Slide 25: LMWI for e-Ring: LER of PEP-II
Estimation of impedance threshold
-average of impedance over bunch power spectrum
Effective impedance in the machine
-Empirically obtained SPEAR-scaling:
-Compare threshold with machine impedance:
Machine
effective
impedance
vs. bunch length
(more realistic
Impedance result
show LER is safe from LMWI)
PEP-II LER | 
 | 3.1
 | 113
 | 1.31
 | 8.0
 | 0.14
(PEP-II CDR)
Threshold
estimation

## Slide 26: LMWI for e-Ring: JLEIC Electron Ring
 | PEP-II (LER) | JLEIC Electron Ring |  | 
 | 3.1 | 4 | 5 | 10
 | 113 | 44.6 | 62.35 | 62.35
 | 1.31 | 2.2 | 2.2 | 2.2
 | 8.0 | 3.64 | 4.55 | 9.1
 | 0.14 | 0.12 | 0.23 | 2.56
Impedance threshold estimation:
JLEIC e-ring is safe from LMBI at nominal energy
At low energy the impedance threshold is comparable to that for
PEP-II LER
Machine impedances:
JLEIC e-ring reuses the RF cavities, vacuum pipe, etc in PEP-II
Further detailed impedance studies need to be done for e-ring in JLEIC

## Slide 27: LMWI for Ion ring: RHIC Proton Beam
Proton
beam
injection
29
250
acceleration
rebucketing
store
(30 sec)
(60 sec)
(20 ms)
(10 hrs)
IBS
 | injection | acceleration | store
 | 29 | 250 | 250
 | 5.4 | 5.4 | 26.6
 | 0.72 | 1.9 | 1.9
 | 4.66 | 0.54 | 2.65
 | 5.2 | 2.1 (1.6) | 7.9
(illustration not to scale)
Estimated
impedance
threshold
Machine impedance:
safe
Bunch spectrum around 400 MHz,
(RHIC/AP/36)

## Slide 28: LMWI Threshold for RHIC Gold Beam
Gold
beam
injection
11
100
acceleration
rebucketing
store
(114 sec)
(6.5 sec)
(20 ms)
(10 hrs)
IBS
(illustration not to scale)
safe
(53 sec)
Estimated
impedance
threshold
Machine impedance
safe
safe
safe
(RHIC/AP/36)

## Slide 29: LMWI for Ion Ring: JLEIC Booster Ring
Proton
beam
accumulation
2
acceleration
Emittance
reduction
extraction
(cooling for ions)
(cooling)
(illustration not to scale)
Estimated
impedance
threshold
acceleration
 | injection
 | 2
 | 0.49
 | 10
 | 2
 | 10.2
Estimating impedance threshold
Need bunch longitudinal
phase space evolution for
the whole cycle
Machine impedance
Need impedance studies
for the booster
8
May be susceptible to space charge impedance

## Slide 30: LMWI Threshold for JLEIC Ion Collider Ring
Proton
beam
stacking
29
250
acceleration
Bunch splitting?
store
(cooling)
Barrier bucket?
 | store
 | 100
 | 15.3
 | 6.45
 | 3
 | 23.8
(illustration not to scale)
Estimated
impedance
threshold
(cooling)
Safe here
Estimating impedance threshold
Need (1) bunch formation
scheme (2) know bunch
longitudinal phase space
evolution for the whole cycle
Machine impedance
Need impedance studies
for ion ring

## Slide 31: Summary
General physics of longitudinal single-bunch instability is discussed.
Initial estimation is started for LMWI-imposed impedance thresholds for e-ring and ion rings in the JLEIC design
Space-charge impedance at low energy may cause concern
The estimations are compared with similar studies in PEP-II for e-ring and in RHIC for ion rings.
In most scenarios JLEIC is safe from LMWI. However, because of unique feature of JLEIC, caution is needed.
  wide energy range and ion species
  electron cooling
  transition crossing
  Etc
Further information are required for a more complete study
  Bunch formation scheme for the ion beams
  Evolution of bunch longitudinal phase space distribution for the whole cycle
  Machine impedance studies