## Slide 1: Progress Report on the Ultra-fast Harmonic Kicker Cavity Design and Beam Dynamic Simulation
Yulu Huang1,2
H. Wang1, R. A. Rimmer1, S. Wang1
1.Thomas Jefferson National Accelerator Facility , Newport News, VA,23606
2.Institute of Modern Physics ,Chinese Academy of Science, Lanzhou, Gansu,730000

## Slide 2: Outline
Fast Kicker Requirements for the JLEIC
Kicker Waveform
  Challenges and Solutions
  Beam Dynamics Tracking for One Kicker Scheme
  Beam Dynamics Tracking for Two Kicker Scheme
Kicker Cavity Design
    Multi-Cavity Kick-Drift Model Tracking
    Prototype Cavity Progress
Conclusion
Acknowledgement

## Slide 3: Kicker Requirements for the JLEIC
Electron cooling is essential for achieving high luminosity
High energy bunched electron cooling is part of multi-phased cooling scheme of JLEIC
To achieve very high current for bunched beam cooling in the future high luminosity upgrade, a circulator ring was adopted to reuse the electron bunches
Electrons circulate 10 to 30 turns in the circulator ring, beam current and bunch repetition frequency in the ERL can be reduced by a factor of 10 to 30
One or two ultra-fast kickers are required for this circulator ring

## Slide 4: Challenges and Solutions
~ns
~10 of ns
Few kV
Few mrad
Pulsed power supplies, especially with these characteristics are beyond state of the art.
An alternative driving method is summing simple cosine waves at sub-frequencies of the final beam repetition frequency to generate a continuous waveform.

## Slide 5: Kick Waveforms to Kick Every 10th Bunch
Chart: Bunch Distance (m)
Bunch | 55 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 55
Chart: Bunch Distance (m)
Bunch | 55 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 55
Chart: Bunch Distance (m)
Bunch | 55 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 55
Chart: Bunch Distance (m)
Bunch | 55 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 55
10 Harmonics+DC offset
9 Harmonics+DC offset

## Slide 6: One Kicker Scheme Tracking
P [MeV/c] | 55
εx, εy [nm] | 10
βx, βy [m] | 10
σs [cm] | 3
σΔp/p | 3e-4
f [MHz] | 476.3
n | 10
Vkick [kV] | 55
Incoming bunch
Outgoing bunch
kicker
Monitor
Transverse effects on kicked and unkicked bunches in a circulator ring simulated using ELEGANT
Circulator ring approximated with 1 turn linear transfer matrix
Kicker waveform generated using a series of zero-length RF deflectors with appropriate frequencies, phases, and amplitudes
Monitor was put after the kicker
Tracking parameter get from Amy

## Slide 7: One Kicker Tracking Result
Flat-Top
Zero-Gradient
Equal-Amplitude
Lease-Modes

## Slide 8: Emittance Growth During Recirculate
Chart: Turn-by-turn Normalized Horizontal Emittance for One-Kicker Scheme
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Flat-Top | 1.0722e-06 | 1.9388e-06 | 2.2782e-06 | 2.4212e-06 | 2.4647e-06 | 2.4766e-06 | 2.5252e-06 | 2.6944e-06 | 3.1083e-06 | 4.7243e-06 | 4.7243e-06
Zero-Gradient | 1.1211e-06 | 1.0981e-06 | 1.0952e-06 | 1.0951e-06 | 1.096e-06 | 1.0976e-06 | 1.0999e-06 | 1.1033e-06 | 1.1097e-06 | 1.1349e-06 | 1.1306e-06
Least-Modes | 1.0947e-06 | 1.8762e-06 | 1.4371e-06 | 1.5823e-06 | 1.5473e-06 | 1.5544e-06 | 1.4844e-06 | 1.7201e-06 | 1.2509e-06 | 2.4649e-06 | 2.427e-06
Equal-Amplitude | 1.3113e-06 | 2.0954e-06 | 2.6739e-06 | 2.9528e-06 | 3.0096e-06 | 2.9449e-06 | 2.9162e-06 | 3.121e-06 | 3.7389e-06 | 5.1604e-06 | 5.3151e-06

## Slide 9: Two Kicker Scheme Tracking
Incoming bunch
Outgoing bunch
Kicker 1
Monitor 1
Kicker 2
Recirculating bunch
Pi Matrix
(180 degree phase advance in x-x’ plane)
x
x’
x
x’
-1 mrad
1 mrad
x’
x’
~0 mrad
~0 mrad
x
x
x’
x
Monitor 2
Monitor 3
Recirculating bunch

## Slide 10: Two Kicker Tracking Result
Flat-Top
Zero-Gradient
Equal-Amplitude
Least-Modes
Monitor 1
Monitor 1
Monitor 1
Monitor 1
Monitor 2
Monitor 2
Monitor 2
Monitor 2
Monitor 3
Monitor 3
Monitor 3
Monitor 3

## Slide 11
Passing through the Pi matrix
Monitor 2
Monitor 3
180 degree phase advance in x-x’ plane

## Slide 12
Emittance Growth During Recirculate
Chart: Turn-by-turn Normalized Horizontal Emittance for Two-Kicker Scheme
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Flat-Top | 1.0741e-06 | 1.0741e-06 | 1.0741e-06 | 1.0741e-06 | 1.0741e-06 | 1.0741e-06 | 1.0741e-06 | 1.0741e-06 | 1.0741e-06 | 1.0741e-06
Zero-Gradient | 1.126e-06 | 1.1261e-06 | 1.1261e-06 | 1.1261e-06 | 1.1261e-06 | 1.1261e-06 | 1.1261e-06 | 1.1261e-06 | 1.1261e-06 | 1.1262e-06
Least-Modes | 1.0885e-06 | 1.0885e-06 | 1.0884e-06 | 1.0884e-06 | 1.0884e-06 | 1.0884e-06 | 1.0884e-06 | 1.0884e-06 | 1.0884e-06 | 1.0884e-06
Equal-Amplitude | 1.3266e-06 | 1.3273e-06 | 1.327e-06 | 1.3271e-06 | 1.3271e-06 | 1.3271e-06 | 1.327e-06 | 1.3272e-06 | 1.3269e-06 | 1.3275e-06

## Slide 13: Kicker Cavity Model
5 harmonics 47.63MHz1,3,5,7,9
3 harmonics 47.63MHz2,6,10
1 harmonics 47.63MHz4
1 harmonics 47.63MHz8
Mode (MHz) | FFT Kick Voltage (kV) | CST Trans. Shunt Impedance (Ω) | Dissipated Power (W)
47.63 | 13.711 | 7.13E6 | 26.37
95.26 | 12.462 | 1.14E7 | 13.62
142.89 | 10.532 | 4.09E6 | 27.12
190.52 | 8.1290 | 1.35E7 | 4.89
238.15 | 5.5030 | 3.14E6 | 9.64
285.78 | 2.9170 | 6.09E6 | 1.40
333.41 | 0.6300 | 2.65E6 | 0.15
381.04 | -1.2090 | 1.65E7 | 0.09
428.67 | -2.4320 | 2.40E6 | 2.46
476.3 | -3.0110 | 4.57E6 | 1.98
DC | 8.2760 |  | 
Total | 55.508 | 3.56E7 | 87.72

## Slide 14: Multi-Cavity Kick-Drift Model
X’
X
1 mrad
Incoming bunch
Outgoing bunch
Recirculating bunch

## Slide 15
Monitor 3
Monitor 2
Monitor 1
Monitor 1
Monitor 2
Monitor 3
Multi-Cavity Kick-Drift Tracking

## Slide 16
Monitor 1
Monitor 3
Monitor 2
Monitor 1
Monitor 2
Monitor 3
Multi-Cavity Kick-Drift Tracking

## Slide 17: Emittance Growth During Recirculate
Chart: Turn-by turn Normalized Horizontal Emittance for Multi-Cavity Scheme
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
Normalized Horizontal Emittance | 1.0741e-06 | 1.0986e-06 | 1.0915e-06 | 1.0896e-06 | 1.0943e-06 | 1.0913e-06 | 1.0893e-06 | 1.097e-06 | 1.0848e-06 | 1.1611e-06
(Flat-Top Scheme)
Initial Normalized Emittance

## Slide 18: Half-Scale Prototype Cavity
Engineering drawings were already finished
The material is already delivered

## Slide 19: Conclusions
An Ultra-fast , high repetition rate kicker was conceptual developed.
Several kick waveform were discussed with the beam dynamics tracking in ELEGANT.
A series harmonic kicker cavities with great power efficiency were designed to generate such kind of kick waveform. Beam dynamics tracking is also studied for this multi-cavities scheme.
An half scale prototype cavity is under manufactured.
A 3-D bead-pull system is set up for the future bench test

## Slide 20: Acknowledgement
Acknowledge to Amy Sy for the help on ELEGANT tracking!