## Slide 1: Vlasov Analysis of Microbunching Gain for Magnetized Beams
Cheng-Ying Tsai
September 12, 2016
NAPAC’16 at Chicago

## Slide 2: Outline
Introduction: micro-bunching instability (MBI)
Motivation: early design of JLEIC Circulator Cooling Ring
Theory of MBI for magnetized beams
Example
Summary and Possible future work

## Slide 3: Outline
Introduction: micro-bunching instability (MBI)
Motivation: early design of JLEIC Circulator Cooling Ring
Theory of MBI for magnetized beams
Example
Summary and Possible future work

## Slide 4: Micro-bunching instability (MBI)
Physical mechanism:
  Heifets, Stupakov, and Krinsky, PRST-AB 5, 064401 (2002)
  Huang and Kim, PRST-AB 5, 074401 (2002)
MBI can be an issue for linac-based machines, e.g. FEL light sources.
MBI can be a more serious issue for recirculating machines, because of many more dipoles (multi-stage amplification).

## Slide 5: Outline
Introduction: micro-bunching instability (MBI)
Motivation: early design of JLEIC Circulator Cooling Ring
Theory of MBI for magnetized beams
Example
Summary and Possible future work

## Slide 6: JLEIC Circulator Cooling Ring
Early design of JLEIC Circulator Cooling Ring (CCR)
  serious microbunching instability
  due to coherent synchrotron radiation (CSR) and longitudinal space charge (LSC)
MEIC Design Report (2012)
Notes: 8 dipoles in the 1st and 3rd arcs
4 dipoles in the 2nd and 4th arcs
total 24 dipoles

## Slide 7: JLEIC Circulator Cooling Ring
Early design of JLEIC Circulator Cooling Ring (CCR)
non-magnetized beam

## Slide 8: JLEIC Circulator Cooling Ring
Early design of JLEIC Circulator Cooling Ring (CCR)
λ = 350 μm (1.2 ps)
  C. -Y. Tsai et al., ERL2015 (TUICLH2034)
Vlasov simulation
Particle tracking

## Slide 9: JLEIC Circulator Cooling Ring
Early design of JLEIC Circulator Cooling Ring (CCR)
  C. -Y. Tsai et al., ERL2015 (TUICLH2034)
λ = 350 μm (1.2 ps)
Vlasov simulation
Particle tracking

## Slide 10: JLEIC Circulator Cooling Ring
Early design of JLEIC Circulator Cooling Ring (CCR)
  C. -Y. Tsai et al., ERL2015 (TUICLH2034)
λ = 350 μm (1.2 ps)
Vlasov simulation
Particle tracking

## Slide 11: JLEIC Circulator Cooling Ring
Early design of JLEIC Circulator Cooling Ring (CCR)
  C. -Y. Tsai et al., ERL2015 (TUICLH2034)
λ = 350 μm (1.2 ps)
Vlasov simulation
Particle tracking

## Slide 12: JLEIC Circulator Cooling Ring
Early design of JLEIC Circulator Cooling Ring (CCR)
  C. -Y. Tsai et al., ERL2015 (TUICLH2034)
λ = 350 μm (1.2 ps)
Vlasov simulation
Particle tracking

## Slide 13: JLEIC Circulator Cooling Ring
Mitigation of micro-bunching instability (MBI)
  Our main interest of this talk
  Larger beam size should help suppress MBI
Improvement of cooling performance
  Cooling beam: low temperature (emittance), beam size comparable to ion beam
  For non-magnetized beam, difficult to meet the requirements simultaneously for small emittance (or low temperature)
  For magnetized beam, easier to satisfy the above requirements while maintaining small Larmor emittance
Slava’s Idea: use magnetized beam
Cathode immersed in solenoid field. Beam has non-zero angular momentum.

## Slide 14: Outline
Introduction: micro-bunching instability (MBI)
Motivation: early design of JLEIC Circulator Cooling Ring
Theory of MBI for magnetized beams
Example
Summary and Possible future work

## Slide 15: Vlasov formalism
Theory is not new
  Heifets, Stupakov, and Krinsky, PRST-AB 5, 064401 (2002)
  Huang and Kim, PRST-AB 5, 074401 (2002)
We extend to more general case of transverse coupled beams

## Slide 16: Vlasov formalism
Model assumptions
Beam dynamics:
  coasting beam approximation
  linear beam transport where

## Slide 17: Vlasov formalism
Model assumptions
Beam dynamics:
  coasting beam approximation
  linear beam transport where
Electrodynamics:
  1-D CSR: assume Derbenev ratio is small
  Note: this assumption can be violated for typical magnetized beam
A. Seryi, Unifying Physics of Accelerators, Lasers and Plasmas

## Slide 18: Vlasov formalism
Define
Phase space distribution function satisfies Vlasov equation

## Slide 19: Vlasov formalism
Define
Phase space distribution function satisfies Vlasov equation
Formulate perturbed phase space distribution (to first order)

## Slide 20: Vlasov formalism
Define
Phase space distribution function satisfies Vlasov equation
Formulate perturbed phase space distribution (to first order)
Micro-bunching can be quantified by
Goal: obtain governing equation for

## Slide 21: Vlasov formalism
To be more specific, given an initial beam phase space distribution,
with density modulation on top of z,
where the beam sigma matrix

## Slide 22: Vlasov formalism
Remember we want to calculate
When we proceed, we will encounter the integration

## Slide 23: Vlasov formalism
Remember we want to calculate
When we proceed, we will encounter the integration
Assume there exists diagonal matrix such that

## Slide 24: Vlasov formalism
Remember we want to calculate
When we proceed, we will encounter the integration
Assume there exists diagonal matrix such that
where
Then
All dynamics information
is contained in D.
Courant-Snyder parameters
for the (coupled) system are
contained in V.

## Slide 25: Vlasov formalism
Putting all together,
where

## Slide 26: Outline
Introduction: micro-bunching instability (MBI)
Motivation: early design of JLEIC Circulator Cooling Ring
Theory of MBI for magnetized beams
Example
Summary and Possible future work
ERL cooler design [S. Benson, JLEIC Collaboration Meeting, Spring 2016]

## Slide 27: Example
achromatic
24 dipoles; 16 inward bending, 8 outward bending
½-indexed dipoles to preserve beam axial symmetry
combined-function dipole to focus/defocus the beam
Name | Value | Unit
Energy | 55 | MeV
Sliced rms energy spread | 1.5 × 10-4 | 
Chirp, h | 4.645 | m-1
Bunch charge | 420 | pC
Initial/final bunch (peak) current | 22.5/6.3 | A
Compression/Decompression factor | 0.28/3.57 | 
4-D geometric emittance ε4D | 1.11 × 10-5 | cm

## Slide 28: Particle tracking
achromatic
24 dipoles; 16 inward bending, 8 outward bending
½-indexed dipoles to preserve beam axial symmetry
combined-function dipole to focus/defocus the beam

## Slide 29: Particle tracking
achromatic
24 dipoles; 16 inward bending, 8 outward bending
½-indexed dipoles to preserve beam axial symmetry
combined-function dipole to focus/defocus the beam

## Slide 30: Vlasov simulation
λ = 300 μm

## Slide 31: Discussion
Smearing effect due to R51
Effective phase mixing when

## Slide 32: Discussion
Smearing effect due to R51
Effective phase mixing when
Our Example:
Early design of CCR:

## Slide 33: Outline
Introduction: micro-bunching instability (MBI)
Motivation: early design of JLEIC Circulator Cooling Ring
Theory of MBI for magnetized beams
Example
Summary and Possible future work

## Slide 34: Summary and Possible future work
Extend Vlasov approach to micro-bunching for magnetized beams
Demonstrate MBI gains for a magnetized-beam transport arc
Results benchmarked against particle tracking simulation
The arc design does not show MBI gain growth (gain ≈ 1)
Larger beam size provides effective suppression of MBI
Parametric dependencies of MBI for magnetized beams, e.g. angular momentum
More aspects of MBI under study (see also THPOA35)
More complete analysis can be done when full-ring lattice is available
Extend the formalism to nonlinear beam transport

## Slide 35: Thank you for your attention

## Slide 36: Acknowledgements
Thanks to my advisors, co-authors for their kind support, insights, discussion and stimulation:
  Rui Li (JLab) and Mark Pitt (Virginia Tech)
  Steve Benson, Slava Derbenev, Dave Douglas, Chris Tennant, He Zhang, Yuhong Zhang (JLab)
Thanks to NAPAC’16 graduate student travel funds
This material is based on work supported by the U.S. Department of Energy, Office of Science, Office of Nuclear Physics under contract DE-AC05-06OR23177.

## Slide 37: BACKUP SLIDES

## Slide 38: Vlasov simulation
λ = 300 μm

## Slide 39: Current dependence of maximal gain
The new ERL cooler design is for weak electron cooling. For comparison, if we increase the bunch charge (i.e. peak bunch current), how about the current dependence of maximal MBI gain?
Note: only steady-state CSR effect is considered.

## Slide 40: MEIC CCR with 420 pC
For comparison, if the bunch charge is reduced to 420 pC, same as that for the new arc design, how about the MBI gain curve for (old) MEIC CCR?
Note: only steady-state CSR effect is considered.
λ = 350 μm (1.2 ps)

## Slide 41: Benchmarking for MEIC CCR x10 εx & εy
C. -Y. Tsai et al., JLAB-TN-16-030

## Slide 42: More aspects of microbunching