## Slide 1: JLEIC Main Parameters with Strong Electron Cooling
Yuhong Zhang
Jan. 12, 2017

## Slide 2: Motivations
The current baseline and main parameters
  Right before the cost review (Jan. 2015)
  Lowering cost and technical risk was the main driving force.
  Cost optimization measures: PEP-II magnets/vacuum chambers
  PEP-II RF (both cavities and power sources)
  Super-ferric magnets,
  Eliminating the large booster
  (Short ion linac for lower energy)
  Risk reduction measures: Weak cooling (single pass ERL cooler)
Performance was compromised
  Large electron emittance (large PEP-II dipoles)
  Large proton/ion emittance (weak cooling)
  Lower emittance: up to 4x1033 (full acceptance detector), and
  8x1033 for high luminosity detector
  < 1034 for any type of detectors

## Slide 3: Motivations
EIC science
  NSAC LRP completed, NAS review is in progress
  Demands higher luminosity (>1034) on Day 1
  CM energy: current baseline up to 63 GeV
  EIC White Paper up to 100 GeV
  eRHIC (both linac-ring & ring-ring) aims for up to 140 GeV
  (Can we match it?)
Accelerator
  Electron ring study: evaluation of small emittance design based on new magnets
  Cooler studies: better understanding of transport/manipulation of magnetized
  electron beam, cooling ring design
  RF fast kicker: 10-turn developed, 20-turn seems feasible
  IR design: smaller detector spaces: proton 7/7 m  3.5/7 m,
  electron 4.5/4.5 m  3.2/3 m (~1.7 m)
  Dynamic aperture: good progress and large aperture achieved
  Ion beam formation: scheme developed, space charge mitigation

## Slide 4: Highlight of New Baseline
New electron ring: new magnets, same footprint
reaches 12 GeV  69 GeV CM
two optics designs (FODO and TME)
same SR (10 kW/m, ~10MW), twice accelerating cavities
Strong cooling is back: circulator cooler ring,
1 to 2 A current in cooling channel
up to 20 circulation, 50 to 100 mA current in ERL
Higher ion current: 500 mA  750 mA (up to 50% luminosity increase)
(this is very substantial change, seems OK with ion
injector/DC cooling, bunched cooling needs study)
Smaller beta-star: β*y 2 cm  1.2 cm (up to 67% luminosity increase)
eliminating “full-acceptance” and “high luminosity” labels
both detectors for Full-Acceptance” and “High-Luminosity”

## Slide 5: JLEIC Baseline Parameters
CM energy | GeV | 21.9 (low) |  | 44.7 (medium) |  | 63.3 (high) | 
 |  | p | e | p | e | p | e
Beam energy | GeV | 40 | 3 | 100 | 5 | 100 | 10
Collision frequency | MHz | 476 |  | 476 |  | 476/4=119 | 
Particles per bunch | 1010 | 0.98 | 3.7 | 0.98 | 3.7 | 3.9 | 3.7
Beam current | A | 0.75 | 2.8 | 0.75 | 2.8 | 0.75 | 0.71
Polarization | % | 80 | 80 | 80 | 80 | 80 | 75
Bunch length, RMS | cm | 3 | 1 | 1 | 1 | 2.2 | 1
Norm. emitt., hor./vert. | μm | 0.3/0.3 | 24/24 | 0.5/0.1 | 54/10.8 | 0.9/0.18 | 432/86.4
Horizontal & vertical β* | cm | 8/8 | 13.5/13.5 | 6/1.2 | 5.1/1 | 10.5/2.1 | 4/0.8
Vert. beam-beam param. |  | 0.015 | 0.092 | 0.015 | 0.068 | 0.008 | 0.034
Laslett tune-shift |  | 0.06 | 7x10-4 | 0.055 | 6x10-4 | 0.056 | 7x10-5
Detector space, up/down | m | 3.6/7 | 3.2/3 | 3.6/7 | 3.2/3 | 3.6/7 | 3.2/3
Hourglass(HG) reduction |  | 1 |  | 0.87 |  | 0.75 | 
Luminosity/IP, w/HG, 1033 | cm-2s-1 | 2.5 |  | 21.4 |  | 5.9 | 

## Slide 6: Playing Same Luminosity Tricks
JLEIC baseline luminosity peaks around 4 x 100 GeV (40 GeV CM)
At low CM energy  both beam energies are low
  Electron: 3~4 GeV, proton: 30~40 GeV
  electron can deliver high current 3 A or above,
  Ion bunch is limited by space charge effect
  Making the bunch length can hold more charges, 1cm3cm  3 times q
  Stronger hour-glass effect: ~10% loss  ~30% loss (net gain)
  Beam dynamics (eg. beam-beam vs. synch-betatron) needs study
At high CM energy  both beam energies are high
  Electron: 8~12 GeV, proton: 100 GeV
  Ion space charge is no longer problem
  Electron current (bunch charge) is limited by strong SR
  Reducing the bunch frequency would boost luminosity L~n1n2fb ~ I1I2/fb
  However, requires even higher cooling bunch intensity (average current same)
  Electron emittance increases, to match beam spot at IP, proton emittance can be much large (requiring less cooling)

## Slide 7: Upgrade 100 GeV and 140 GeV CM Energy
Present upgrade path: 6 T  200 GeV proton (69 GeV CM)
Question: can JLEIC reach 140 GeV CM Energy?
Answer: without upgrade the electron ring and CEBAF
it needs 400 GeV proton to reach 140 GeV CM
It needs 12 T SC magnets

## Slide 8: JLEIC e-p Luminosity

## Slide 9: JLEIC e-p Luminosity

## Slide 11: e-p Luminosity
Chart: 
| 21.9 | 27.9 | 34.700000000000003 | 40 | 44.7 | 49 | 56.6 | 63.3 | 69.3
Max dipole field: 3 T | 2.48 | 6.86 | 16.48 | 22.27 | 21.4 | 18.41 | 9.99 | 5.87 | 2.37
Max dipole field: 6 T | 2.48 | 6.86 | 16.5 | 32.28 | 37.43 | 22.46 | 7.99 | 3.24
Max dipole field: 8.4 T" | 2.48 | 6.86 | 16.5 | 32.28 | 43.84 | 44.12 | 37.55 | 16.83 | 7.96 | 3.24
Max dipole field: 12 T | 2.48 | 6.86 | 16.5 | 32.28 | 43.84 | 47.64 | 44.27 | 36.71 | 18.73 | 8.13 | 3.29
40 GeV x 3 GeV
100 GeV x 5 GeV
100 GeV x 10 GeV