## Slide 1: Selected Summary of Review Report for JLEIC the Design
Rui Li
2/23/17
JLEIC R&D Meeting

## Slide 2: About JLEIC Design
NP
  ECM<100GeV
  (NSAC LRP requires minimum of 100GeV)
  “Argument presented to the panel indicated that significant new physics cold be accessed at ECM< 100 GeV, but the panel was unable to judge the merit of this point”.
IR
  Pulse structure effect on nuclear experiment
  Crab with large VRF not tested for ion

## Slide 3
Luminosity
  JLEIC is far from beam-beam limit
  Luminosity can increase by factor of 2 to 3
e-Cooler
  Longitudinal cooling, need to transfer to the transverse cooling
  Ensure the ongoing pulsed beam cooling are relevant to the goal of hadron cooling for JLEIC
  Continue the fast cooling for bunched beam, while study the alternate approach of CeC
Figure-8
  Potential benefit on polarization is well recognized
  Need validation by theory and simulation
  Not efficient use of bend
  Increase SR, limit Ie or Ee

## Slide 4
ERL
  Iave beyond state-of-art
  Consider thermionic gun
  Angular momentum effects on BBU stability critierion
Beam-Beam
  Collision with crabbing
  Multibunch collision through gear change
  Need to validate the scheme through beam simulation
Polarization
  Polarized 3He source

## Slide 5
Magnet
  Superferric magnet now at B=2.5 T. JLEIC needs B=6T
  Risk at reaching high electron energy and maximizing luminosity
Collective Effects
  E-cloud: 2-stream instabilities, maybe counteracted by feedback
  E-cloud mitigation scheme (work with universities)
  Instability thresholds
  IBS
  Beam halo and losses
  Feedback (KEKB not using longitudinal feedback often)

## Slide 6
Simulations
Simulation tools for beam dynamics studies of proposed EIC concepts
need to be developed to include the many important physics aspects
of these complex machines
Beam-beam effects
instability thresholds
detector backgrounds
intra-beam scattering
beam halo formation and losses
beam crabbing
Feedback systems,
Cooling system
will all eventually need to be modeled and well understood
using validated codes, prior to the final design of lattices and hardware.

## Slide 7
More Comments on Simulations
All EIC concepts need to be modeled and beam dynamics well
understood using multi-physics, high-resolution codes, validated as
much as practical using experimental data from other facilities,
prior to the final design of the hardware. Not having high-
fidelity models of EIC performance presents a risk in
achieving the required luminosity. Conversely, extrapolation
from simulations or proof of principle demonstrator experiments
to a full-blown implementation over orders of magnitude of
critical parameters can introduce risk.

## Slide 8
Collaboration with BNL
  Development of new simulation tools
  Beam-beam with crabbed bunch
  High current ERL
  SRF