## Slide 1: JLEIC Ion Beam Formation options for 200 GeV
Jiquan Guo, Yuhong Zhang

## Slide 2: Current JLEIC Injection Chain Baseline (100 GeV design)
Current JLEIC ion injection chain has only one booster
  Reasonable ramping range in the booster and the colliders for 100 GeV
  less magnet ramping cycles makes the operation simple and fast
  8 GeV collider proton injection energy is less challenging for DC cooling
  space charge during the injection stage in both the booster (100 MeV Pb67+ or 285 MeV p) and the collider ring (~2 GeV Pb82+ and 8 GeV p) will be marginal and requires larger beam pipe aperture. Cooling during these stages has to be minimum, even though the DC coolers are very efficient at lower energy.
Baseline has 26 booster cycles:
  Each cycles has stages of accumulation (with DC cooling), capture, ramp, bunch length compression (from ~1/7 to ~1/28 of collider circumference, probably also pre-split), transfer
  DC cooling in collider ring during staging is highly desired
  After 26 booster cycles, collider ring will ramp to ~20GeV then perform binary bunch split.
ion sources
SRF Linac
Booster with DC cooler
collider ring with BB/DC cooler
285MeV H-
100MeV Pb67+
~8GeV H+
2-2.4GeV Pb67+
<=100GeV H+
<=40GeV Pb82+
Multi-turn injection
Bucket-to-bucket transfer
H- Strip
Pb Strip

## Slide 3: Injection Chain Options for 200 GeV
Keep the linac and booster as it is, increase the energy range of the collider ring
  Keep the 8 GeV DC cooling in the collider ring
  Large ramping range of the collider ring (~ factor of 23)
  2GeV Pb82+ space charge tune shift during collider ring injection will be high for 0.5A collider beam current, even with the 100 GeV option
Increase the energy of the booster (~10.5GeV), increase the booster size (or change to racetrack)
  Linac energy could be increased, too
  Do/can we need to increase the booster dipole field to 6T?
Add a pre-booster
  Can reduce linac energy and save some cost on linac (but by how much?)
  Increased ramping cycles and operation complexity
Proton Ek =285 MeV to 200 GeV (p/q=0.785 GeV/c to 201 GeV/c) (Pb p/q/u at 100MeV higher than 0.785GeV/c)
Pb stripping from 67+ to 82+ before entering collider ring (probably the largest strip ratio among all heavy ions)
  Total dipole ramp ratio: 201/0.785×82/67=313=17.7^2:
  Pre-booster scheme: Proton Ek =135 MeV to 200 GeV, total ramp ratio 472=7.8^3
  400 GeV upgrade: total ramp ratio ≈9.8^3
  Main booster energy limited by DC cooler? Or collider ring DC cooling not mandatory if booster energy is high enough?

## Slide 4: Ion Beam Formation Cycles (single booster)
Collider circumference 2255m, final harmonic # Nh=3584(28*2^7), booster circumference 322.2m
Eject the used beam from the collider ring, cycle the magnets
Multi-turn injection of polarized ion from linac to booster (non-polarized for heavy ions)
Capture beam into a bucket (~200m bunch length)
Ramp to an intermediate energy (~2.0GeV proton), perform DC cooling, ramp to ~8GeV (proton)
Compress the bunch length to 56m and split into 2 bunches, 28m each in 40m buckets
Bucket-to-bucket transfer the long bunch into collider ring, each bucket 40m (gap between bunches ~12m, ~40ns for kicker rise time)
Repeat step 2-6 for 2×13 times, each cycle ~1 min, total ~30 min
Ramp collider ring to 8 GeV (ion only). Perform DC cooling. Ramp collider ring to 20GeV
Perform binary bunch splitting up to 7 times to harmonic # Nh=3584 (when colliding high energy/low current electron beam, splitting can be reduced to 5 times to Nh=896), perform bunch length compression
Manipulate the beam to create several extra empty buckets (476 MHz) in the gap (Nh=3576-3584 depending on ion energy, as required by beam synchronization). Ramp to collision energy, turn on 952MHz SRF and BB cooling.
2. Accumulating coasting beam
3. Capture to bucket
4. Accelerate and cool
DC cooler
DC cooler
5. Bunch compression to ~56m, split into 2 bunches
Step 6/7. Bucket-to-bucket transfer to the collider ring and BB cooling, repeat 2×13 times (Nh=56)
BB cooler
2 gaps, 80m
Final bunch train structure in the collider ring
1664 bunches, ~1050m
1664 occupied bunches, ~1050m
Gap of 126-130 empty buckets
Gap of 126-130 empty buckets, ~80m

## Slide 5: Parameters (single booster, 26 cycles)
 | 100 GeV Baseline |  | 100 GeV Baseline+ |  | 200 GeV HE | 
 | proton | Pb | proton | Pb | proton | Pb
Collision Ib (A) | 0.75 | 0.39 | 0.75 | 0.46 | 0.75 | 0.75
Linac Energy (MeV/u) | 285 | 100 | 285 | 100 | 285 | 100
Booster charge state | 1+ | 67+ | 1+ | 67+ | 1+ | 67+
Booster total ion (1010) | 135 | 0.86 | 135 | 1.01 | 135 | 1.65
Booster Bρ inj (Tm) | 2.618 | 4.604 | 2.618 | 4.604 | 2.618 | 4.604
Booster Bρ ext (Tm) | 29.314 | 29.314 | 29.314 | 35.876 | 38-46.5 | 46.5
Booster Ek ext (GeV/u) | 7.9 | 2.04 | 7.9 | 2.651 | 10.5-13 | 3.65
Booster dipole max/min | 11.2 |  | 13.7 |  | 17.76 | 
Booster circumference (m) | 322.2 (3T bend OK) |  | 322.2 (3T?) |  | 322.2 racetrack (or 483.8 F8) | 
Booster inj νlass (70% rect) | 0.082 | 0.041 | 0.100 | 0.060 | 0.100 | 0.097
Booster inj σ (x, y, mm) β=14m | 6.7 | 6.7 | 6.0 | 6.0 | 6.0 | 6.0
Collider Bρ inj (Tm) | 29.314 | 23.952 | 29.314 | 29.314 | 38-46.5 | 38
Collider Bρ max (Tm) | 336.675 |  | 336.675 |  | 670.24 | 
Collision Ek max (GeV/u) | 100 | 38.86 | 100 | 38.86 | 200 | 78.28
Collider dipole max/min | 14.1 |  | 11.5 |  | 17.63 | 
Collider circumference (m) | 2255.34 |  |  |  | 2255.41 | 
Collider inj νlass (σz=bucket/6) | 0.045 | 0.151 | 0.056 | 0.149 | 0.022-0.033 | 0.146
Collider inj σ (x, y, mm) β=14m | 2.0 | 2.6 | 1.8 | 2.15 | 1.4-1.6 | 1.9
Collider DC cool energy (GeV) | 7.9 | 7.9 | 7.9 | 7.9 | 10.5-13 | 10.5
DC cooled νlass (σz=bucket/6) | 0.15 | 0.123 | 0.15 | 0.145 | 0.15 | 0..15
DC cooled εn, x/y (μm), space charge limit | 0.8 | 0.2 | 0.8 | 0.2 | 0.48-0.32 | 0.188
Minimum collision εn, x/y (μm) | 0.3/0.1 | ? | 0.3/0.1 | ? | 0.3/0.1 | ?
Normalized emittance at booster extraction not smaller than booster injection

## Slide 6: Comparing single booster schemes
The parameter differences between the schemes mainly arise from the choice of booster extraction energy
  7.9 GeV energy was chosen in the baseline because the Tevatron 4.3MeV DC cooler is the highest energy proven case. However, the Tevatron DC cooler is not a magnetized cooler, so we can not just lie on that design.
  There are R&D efforts for GSI FAIR on 4-8 MV DC cooler by HIM
The baseline for 100 GeV chose 7.9 GeV proton energy for the booster extraction, and the same booster extraction magnetic rigidity for Pb67+ (2.04 GeV)
  Pb67+ will be stripped into Pb82+ on the way to collider ring, so magnetic rigidity at collider injection lowered. Requiring extra ramp range for the collider magnets
  Space charge for Pb82+ injected into collider ring is marginal (need large beam size)
  Space charge for proton is OK for injection, but limits the utilization of the power of DC cooling
Baseline+ for 100 GeV case increases booster extraction energy for Pb67+, so the collider inj magnetic rigidity for Pb82+ 2.65GeV will be the same with 7.9GeV proton
  Pb67+ space charge improves. Beam sizes reduce at inj of both the booster and collider.
  Proton still under-utilizes DC cooling (can’t cool 0.5-075A beam to ~0.2μm-rad)
HE (200 GeV) can still use the single booster scheme with higher booster energy
  Booster Pb67+ extraction chosen at 3.65 GeV to make both booster/collider ramp ratio to ~17.7
  Magnet determines that proton extraction energy can be in range of 10.5-13 GeV, we choose the low end of 10.5 GeV to minimize cooler requirement
  Due to the higher magnet rigidity for the booster, we can choose: 3T magnets 483m figure-8 ring, 3T magnets 322m racetrack (both cases dipole length is 30% of circumference), or 6T 282m Figure-8.
  Space charge will be better with higher energy.

## Slide 7: Two booster scheme: work under progress
Possible advantages:
  Compatible with the 400 GeV upgrade
  If collider ring injection energy too high for DC cooling, we can apply DC cooling in the large booster before transfer into the main ring
  Smaller aperture in the large booster
  Avoid γT jump (even for heavy ion in the collider ring it is possible)
Possible disadvantages:
  More ramping cycles in the pre-booster

## Slide 8: Parameters (With pre-booster 200GeV)
 | 200GeV HE | 
 | proton | Pb
Collision Ib (A) | 0.75 | 
Linac Energy (MeV/u) | 135 | 40
Pre-Booster charge state | 1+ | 67+
Pre- Booster Bρ inj (Tm) |  | 
Pre-Booster Bρ ext (Tm) |  | 
Pre-Booster Ek ext (GeV/u) |  | 
Pre-Booster dipole max/min |  | 
Pre-Booster circumference (m) | 80.6 | 
Pre-Booster inj νlass (70% rect) |  | 
Pre-Booster inj σ (x, y, mm) β=14m |  | 
Booster charge state | 1+ | 82+
Booster Bρ inj (Tm) |  | 
Booster Bρ ext (Tm) |  | 
Booster Ek ext (GeV/u) |  | 
Booster dipole max/min |  | 
Booster circumference (m) |  | 
Booster inj νlass (70% rect) |  | 
Booster inj σ (x, y, mm) β=14m |  | 
 | 200GeV HE | 
 | proton | Pb
Collider charge state | 1+ | 82+
Collider Bρ inj (Tm) |  | 
Collision Ek max (GeV/u) | 200 | 78.28
Collider Bρ max (Tm) |  | 
Collider dipole max/min |  | 
Collider circumference (m) | 2255.34 | 
Collider inj νlass (σz=bucket/6) |  | 
Collider inj σ (x, y, mm) β=14m |  | 
Collider DC cool energy (GeV) | NA | NA
DC cooled νlass (σz=bucket/6) |  | 
DC cooled σ (x, y, mm) β=14m |  | 
Work under progress

## Slide 9: 200GeV with pre-booster, binary splitting
Pre-booster ~120m (3T racetrack). Booster 280-360m (6T Figure 8, can upgrade to 12T with 400GeV upgrade), main ring ~2255m
52-54 pre-booster cycles. Each cycle start with ramping magnet, accumulate in pre-booster (135MeV p, 40MeV Pb67+), then capture and accelerate to 4GeV p/0.9GeV Pb. Compress bunch length to 28m, extract to main booster. Pb67+ stripped to Pb82+
After 6-7 pre-booster cycles, the main booster is almost full. Accelerate to 10-13GeV and perform DC cooling. Ramp to ~16GeV, transfer to collider ring
Repeat 8 main booster cycles to fill the collider ring
Binary split in the collider ring. Then accelerate to collision energy

## Slide 10: Parameters (With pre-booster, capable for 400GeV)
 | 400GeV HE | 
 | proton | Pb
Collision Ib (A) |  | 
Linac Energy (MeV/u) | 135 | 40
Pre-Booster charge state | 1+ | 67+
Pre- Booster Bρ inj (Tm) |  | 
Pre-Booster Bρ ext (Tm) |  | 
Pre-Booster Ek ext (GeV/u) |  | 
Pre-Booster dipole max/min |  | 
Pre-Booster circumference (m) |  | 
Pre-Booster inj νlass (70% rect) |  | 
Pre-Booster inj σ (x, y, mm) β=14m |  | 
Booster charge state | 1+ | 82+?
Booster Bρ inj (Tm) |  | 
Booster Bρ ext (Tm) |  | 
Booster Ek ext (GeV/u) |  | 
Booster dipole max/min |  | 
Booster circumference (m) |  | 
Booster inj νlass (70% rect) |  | 
Booster inj σ (x, y, mm) β=14m |  | 
 | 400GeV HE | 
 | proton | Pb
Collider charge state | 1+ | 82+
Collider Bρ inj (Tm) |  | 
Collision Ek max (GeV/u) | 200 | 
Collider Bρ max (Tm) |  | 
Collider dipole max/min |  | 
Collider circumference (m) | 2255.34 | 
Collider inj νlass (σz=bucket/6) |  | 
Collider inj σ (x, y, mm) β=14m |  | 
Collider DC cool energy (GeV) | NA | NA
DC cooled νlass (σz=bucket/6) |  | 
DC cooled σ (x, y, mm) β=14m |  | 
Work under progress

## Slide 11: 400GeV with pre-booster, barrier bucket splitting?
Pre-booster ~120m (3T racetrack). Booster 362m (up to 12T Figure 8), main ring ~2255m
48 pre-booster cycles. Each cycle start with ramping magnet, accumulate in pre-booster (135MeV p, 40MeV Pb67+), then capture and accelerate to ~4GeV p/0.9GeV Pb. Compress bunch length to 28m, extract to main booster. Pb67+ stripped to Pb82+
After 8 pre-booster cycles, the main booster is full. Accelerate to ~13GeV and perform DC cooling. Debunch within barrier bucket of ~340m, then rebunch to 119-952MHz bunches. Accelerate to ~30GeV. Bucket to bucket transfer to the main ring
Repeat 6 main booster cycles to fill the collider ring with 4x9m+2x80m gaps between the long bunch trains (4x9m more gaps than binary splitting in the collider ring, will reduce luminosity by <2%). 9m gap assumes injection/extraction kicker rise time of 30ns, which is in line with eRHIC R&D goal.
  80m gaps work as abort gaps which needs longer kicker rise time, and also matches the 2 e-ring gaps
  Each e-ring gap needs to be ~80m, including 40m for injection/abort/ion clearing gap, and 2x20m for transient beam loading compensation.
Might be easier for bunch formation with harmonic change.