## Slide 1: Option 1: Reduced FF Quad Apertures
Same optics and geometry
Quad apertures  6 T / at 200 GeV/c = 37 / 58 / 73 mm (radius)
Quad aperture / distance from IP to quad’s far end = 4.5 / 5.0 / 5.3 mrad
= 10 / 2 cm, at roman pot = 0.95 m

## Slide 2: Option 2: Doubled Detector Space and Halved Crossing Angle
Keep maximum -functions at ~2500 m  same maximum beam size
Quad apertures  6 T / at 200 GeV/c = 50 / 83 / 215 mm (radius)
Quad aperture / distance from IP to quad’s far end = 3.3 / 4.5 / 10.3 mrad
= 28 / 7.5 cm, at roman pot = 0.48 m

## Slide 3: Option 3: Doubled Quad Lengths
Keep maximum -functions at ~2500 m  same maximum beam size
Quad apertures  6 T / at 200 GeV/c = 85 / 152 / 196 mm (radius)
Quad aperture / distance from IP to quad’s far end = 9.1 / 10.0 / 10.5 mrad
= 18 / 2.15 cm, at roman pot = 0.97 m

## Slide 4: Option 4: 1.5x Quad Lengths and 2/3 Crossing Angle
Keep maximum -functions at ~2500 m  same maximum beam size
Quad apertures  6 T / at 200 GeV/c = 72 / 129 / 292 mm (radius)
Quad aperture / distance from IP to quad’s far end = 5.9 / 7.6 / 14.8 mrad
= 24 / 4.4 cm, at roman pot = 0.64 m

## Slide 5: Summary
Option | Quad radii (mm) | Quad (mrad) | at roman pot (m) | (cm) | Luminosity factor
1 | 37 / 58 / 73 | 4.5 / 5.0 / 5.3 | 0.95 | 10 / 2 | 1
2 | 50 / 83 / 215 | 3.3 / 4.5 / 10.3 | 0.48 | 28 / 7.5 | 0.31
3 | 85 / 152 / 196 | 9.1 / 10.0 / 10.5 | 0.97 | 18 / 2.15 | 0.72
4 | 72 / 129 / 292 | 5.9 / 7.6 / 14.8 | 0.64 | 24 / 4.4 | 0.44
Option | Quad radii (mm) |  |  |  | Luminosity factor
1 | 37 / 58 / 73 | 4.5 / 5.0 / 5.3 | 0.95 | 10 / 2 | 1
2 | 50 / 83 / 215 | 3.3 / 4.5 / 10.3 | 0.48 | 28 / 7.5 | 0.31
3 | 85 / 152 / 196 | 9.1 / 10.0 / 10.5 | 0.97 | 18 / 2.15 | 0.72
4 | 72 / 129 / 292 | 5.9 / 7.6 / 14.8 | 0.64 | 24 / 4.4 | 0.44