## Slide 1: HE-JLEIC: Do We Have a Baseline?
Yuhong Zhang
June 5, 2018

## Slide 2: Path to 100 GeV CM Energy
Physics requirement: Preserve high luminosity for CM energy below 69 GeV
Reach 100 GeV CM energy with good luminosity
Preserve full acceptance detections
Design strategy: High CM energy and full acceptance are highest priority
High luminosity at high energy is a plus
Risk, cost and accelerator R&D modest
The same design principles (concepts and
Electron complex: no change / no upgrade of CEBAF
Ion complex: collider ring energy double 100 GeV  200 GeV
  same foot print, double the dipole field: 3 T  6 T
Modification of IR: basically the same,
doubling the quad lengths (longer focusing length)
Polarization: figure-8
High energy ERL cooling: (optional?)

## Slide 3: Ion Collider Ring Magnets
There is a solution in cosine-theta magnets
6 T, Curved, 2 layer coil design has been prototyped and tested (IHEP)
Prototype program required
Need to get more information than what is presented in technical papers
Alternative
  look at lower operating temperture as a means to get a 1 layer coil design (less technical risk for curved magnet, requires higher operating cost for cryogenics)
  look at Nb3Sn to get a 1 layer coil design (higher cost magnets, brittle coil structure, can it be build curved, 4.5 K operation)
SIS 300, a fast-ramping heavy ion synchrotron with a rigidity of 300 T-m, with 6 T, 100 mm coil aperture 2.6 m long SC dipoles, ramped at 1 T/s [2].
The fast ramp rate requires a magnet design that minimizes AC losses and field distortions during ramping.
A two layer cos  magnet design, using a cored Rutherford cable, has been chosen.
Tim Michalski, Ruben Fair,
Renuka Rajput-Ghoshal,
Probir Ghoshal

## Slide 4: Two Booster Injector (with a full size 2nd booster)
Relative higher injection energy into booster rings
High voltage DC cooler is within the state-of-art (4 MeV)
  No need of 8 MeV DC cooling for 15 GeV proton beams,
  there will be no technical risk for DC cooling
The 2nd booster ring ejection energy can be much higher
  20 GeV or even 30 GeV (about 1 T magnet),
  May eliminate transition energy crossing for all ion species at the collider ring
Small aperture magnet for the collider ring
  The injected beam to the collider ring has small emittances/beam sizes
Stacking-cooling ring if no bunched beam ERL cooling
  Stored beam must be replaced frequently due to IBS induced emittance growth
  A new beam could be formed while the collider ring is in operation
  When the used beam is ejected, the already formed new beam in the 2nd booster can be transferred into the collider ring immediate
  The ion beam formation time can reduced from ~30 min to ~1 min.
  This can increase the duty factor and the integrated luminosity.
Yuhong Zhang, Jiquan Guo

## Slide 5: Two Booster Injector: Proton
ion sources
SRF linac
1st booster
collider ring
BB cooling
DC cooling
2nd booster (full size)
DC cooling
Injection: 285 MeV
Accumulation
Accelerate to 8 GeV
Injection: 8 GeV
Stacking 56 long bunches with DC cooling (4 MeV)
Precooling (4 MeV DC)
Accelerate to ~25 GeV
Bunch splitting
Injection: ~25 GeV
Accelerating to collision energy
Bunched beam cooling
Yuhong Zhang, Jiquan Guo
Multi-turn injection accumulation
Bunch splitting
285 MeV
25 GeV
Up to 200 GeV
DC cooler 4.3 MeV
BB ERL cooler
up to 109 MeV
collider ring
1st booster
proton
Stacking,
Pre-cooling
8 GeV
Fast ramp
emittance preservation
2nd booster
Energy
Ramp: 6.4
Ramp: 3.6
Ramp: 7.8

## Slide 6: Two Booster Injector: Ion Lead
ion sources
SRF linac
1st booster
collider ring
BB cooling
DC cooling
2nd booster (full size)
DC cooling
Injection: 100 MeV
Accumulation with cooling
Acceleration to 2 GeV
Injection: 2 GeV
Stacking 56 long bunches with DC cooling
Accelerate to ~8 GeV, then pre-cooling
Bunch splitting
Acceleration to 9.35 GeV
Injection: 9.35 GeV
Bucket-to-bucket transfer
Acceleration to ~20 GeV
Accelerate to collision energy
Bunched beam cooling
Multi-turn injection accumulation
Pre-cool
Bunch splitting
100 MeV/u
~20 GeV/u
Up to 78.3 GeV/u
DC cooler 4.3 MeV
BB ERL cooler
up to 42.6 MeV
collider ring
1st booster
Lead Ion
Stacking,
emittance preservation
2 GeV/u
DC cooler
1.1 MeV
8 GeV/u
Fast ramp
emittance preservation
2nd booster
Energy
9.35 GeV/u
DC cooler 55 keV
Ramp: 6.4
Ramp: 3.61
Ramp: 7.8
Yuhong Zhang, Jiquan Guo

## Slide 7: Interaction Region
Keep maximum -functions at ~2500 m  same maximum beam size
Quad apertures  6 T / at 200 GeV/c = 85 / 152 / 196 mm (radius)
Quad aperture / distance from IP to quad’s far end = 9.1 / 10.0 / 10.5 mrad
= 18 / 2.15 cm, at roman pot = 0.97 m
 |  | Quad radii (mm) | Quad (mrad) | at roman pot (m) | (cm) | Luminosity reduction factor
1 | Reduced FFQ apertures | 37 / 58 / 73 | 4.5 / 5.0 / 5.3 | 0.95 | 10 / 2 | 1
2 | Doubled detector space, halved crossing angle | 50 / 83 / 215 | 3.3 / 4.5 / 10.3 | 0.48 | 28 / 7.5 | 0.31
3 | Doubled quad lengths | 85 / 152 / 196 | 9.1 / 10.0 / 10.5 | 0.97 | 18 / 2.15 | 0.72
3.1 | Cut 1st FFQ in half, use 1st half only at < 65 GeV |  |  |  | 7.5 / 2 | 1.15
4 | 1.5 quad lengths, 2/3 crossing angle | 72 / 129 / 292 | 5.9 / 7.6 / 14.8 | 0.64 | 24 / 4.4 | 0.44
 |  | Quad radii (mm) |  |  |  | Luminosity reduction factor
1 | Reduced FFQ apertures | 37 / 58 / 73 | 4.5 / 5.0 / 5.3 | 0.95 | 10 / 2 | 1
2 | Doubled detector space, halved crossing angle | 50 / 83 / 215 | 3.3 / 4.5 / 10.3 | 0.48 | 28 / 7.5 | 0.31
3 | Doubled quad lengths | 85 / 152 / 196 | 9.1 / 10.0 / 10.5 | 0.97 | 18 / 2.15 | 0.72
3.1 | Cut 1st FFQ in half, use 1st half only at < 65 GeV |  |  |  | 7.5 / 2 | 1.15
4 | 1.5 quad lengths, 2/3 crossing angle | 72 / 129 / 292 | 5.9 / 7.6 / 14.8 | 0.64 | 24 / 4.4 | 0.44
Vasiliy Morozov
Option 3
Option 3.1

## Slide 8: Cooling at Collision
Best result:
Reduce proton beam current to 40% of the nominal value  0.3 A
Dispersion: 1.8/0.3 m, coupling: 24%
Emittance was maintained for one hour.
Not in equilibrium, momentum spread is still decreasing.
Change of the ERL cooler
Injector and merger
Merger cavity twice as strong or half the angle if we go with RF merger.
Linac cryomodule : 1 ⇒ 2
Arcs and beam physics
  Double magnet strength
  Chirper and de-chirper twice the gradient
  Space charge reduced
  CSR and µBI should be about the same
Cooler insertion
  Focusing magnets twice as strong
Exchange region
  Focusing magnets twice as strong
  Kickers twice as strong (4 time the power)
Beam dump may need more acceptance
Do we need ERL cooling?

## Slide 10: JLEIC Baseline
CM energy | GeV | 21.9 (low) |  | 44.7 (medium) |  | 63.3 (high) | 
 |  | p | e | p | e | p | e
Beam energy | GeV | 40 | 3 | 100 | 5 | 100 | 10
Collision frequency | MHz | 476 |  | 476 |  | 476/4=119 | 
Particles per bunch | 1010 | 0.98 | 3.7 | 0.98 | 3.7 | 3.9 | 3.7
Beam current | A | 0.75 | 2.8 | 0.75 | 2.8 | 0.75 | 0.71
Polarization | % | 80 | 80 | 80 | 80 | 80 | 75
Bunch length, RMS | cm | 3 | 1 | 1 | 1 | 2.2 | 1
Norm. emitt., horiz./vert. | μm | 0.3/0.3 | 24/24 | 0.5/0.1 | 54/10.8 | 0.9/0.18 | 432/86.4
Horizontal & vertical β* | cm | 8/8 | 13.5/13.5 | 6/1.2 | 5.1/1 | 10.5/2.1 | 4/0.8
Vert. beam-beam param. |  | 0.015 | 0.092 | 0.015 | 0.068 | 0.008 | 0.034
Laslett tune-shift |  | 0.06 | 7x10-4 | 0.055 | 6x10-4 | 0.056 | 7x10-5
Detector space, up/down | m | 3.6/7 | 3.2/3 | 3.6/7 | 3.2/3 | 3.6/7 | 3.2/3
Hourglass(HG) reduction |  | 1 |  | 0.87 |  | 0.75 | 
Luminosity/IP, w/HG, 1033 | cm-2s-1 | 2.5 |  | 21.4 |  | 5.9 | 
63.3 (high) | 
p | e
100 | 10
476 | 
0.98 | 3.7
0.75 | 0.71
80 | 75
1 | 1
0.9/0.18 | 432/86.4
10.5/2.1 | 4/0.8
0.002 | 0.009
0.031 | 
3.6/7 | 3.2/3
0.86 | 
1.7 |