## Slide 1
Yuhong Zhang, Jefferson Lab, USA
Abstract Jefferson Lab electron-ion collider (JLEIC) is designed to reach high luminosity for physics program. An challenging R&D for JLEIC is development of advanced cooling technologies. Here we present schemes for optimizing JLEIC integrated luminosity performance without cooling of ion beams during collisions.
Thomas Jefferson National Accelerator Facility, Virginia, USA, Managed by the Jefferson Science Associates, LLC for the U.S. Department of Energy
Cooling Cancels IBS (<150 GeV)
Thank Ya. Derbenev, P. McIntyre for helpful discussions, and V. Morozov, H. Zhang for assistance in IBS estimate
Staged Electron Cooling
Low voltage DC cooling: assisting accumulation
High voltage DC cooling: 6D emittance reduction
High energy ERL cooling: maintain emittance
Many-Small-Bunches for High Lumi.
Beam Design
High repetition rate
Low bunch intensity
Short bunch length
Small emittance
IR Design
Very small β*
Crab crossing
Damping
Synchrotron radiation
Electron cooling
Optimization 1: Short beam store in Ion Collider Ring
KEp=100 GeV, Ip=0.5 A, Iec=1.05 A
 |  | IBS | ECOOL
RH | 1/s | 4.7E-3 | -2.4E-3
RV | 1/s | -1.7E-5 | -2.3E-3
RL | 1/s | 1.2E-3 | -3.0E-3
Adjusting IR optics (β*) of both beams dynamically for
Matching spot size at IP  optimizing beam-beam
Control beam sizes at final focusing quads  satisfying magnet apertures
Instance Luminosity
IBS calculation by JSPEC
30 min
60 min
90 min
120 min
start with 1 µm (by DC cooling)
150 min
180 min
210 min
240 min
Vertical emittance has no growth
Longitudinal IBS effect is modest ~20% growth in 2 h
Initial emittance 1 µm and 0.5 µm
Chart: 
| 0 | 240
Present Baseline design | 3.03 | 3.03
Initial emittance: 1 and 0.5 um | 4.6 | 3.07 | 2.27 | 1.87 | 1.63 | 1.47 | 1.34 | 1.24 | 1.16
Chart: 
| 0 | 240
Present Baseline design | 3.03 | 3.03
Initial emittance: 1 and 0.5 um | 4.6 | 3.07 | 2.27 | 1.87 | 1.63 | 1.47 | 1.34 | 1.24 | 1.16
4.6
3.3
2.6
2.0
2.2
3.8
3.0
2.9
Optimization 2: pre-Cooling
Take advantage of DC cooling at the HE booster
Achieve very small (initial) emittance
Harvest high contribution of initial instant Luminosity
Evolution of Instance Luminosity
30 min
60 min
90 min
120 min
If start with 0.5 / 0.25 µm (prepared by DC cooling)
150 min
180 min
210 min
240 min
Vertical emittance has no growth
Longitudinal IBS effect is modest
IBS calculation by JSPEC codes
Chart: 
| 0 | 240
Present Baseline design | 3.03 | 3.03
Ultimate design | 8.81 | 8.81
"Initial emittance: 0.5 and 0.25 um | 8.38 | 3.99 | 2.76 | 2.21 | 1.91 | 1.7 | 1.54 | 1.43 | 1.33
8.4
3.0
4.8
3.5
2.9
2.6
8.8
6.2
4.0
High contribution
More Optimization Ideas: Beam Reconditioning by DC Cooling
Reconditioning time: should be 5 min or less
Ideally, ramp down/up ~ 1 minute
top-off (optional) ~ a few seconds
DC cooling ~ a couple of mins,
Could be useful if the high energy booster is not full size
Injection Energy
Collision Energy
Bunch Merge
Energy ramp down
Bunch Split
Energy ramp Up
Reconditioning by DC cooling
Collision
Injection
Conclusions
JLEIC integrated luminosity without cooling during collision is still able to meet EIC science requirement.
The luminosity performances can be improved with short beam store, pre-cooling by a DC cooler, reducing bunch repetition rate, full size high energy booster, beam-beam leveling and un-matching of beam spot sizes at IP.
Ion Beam Formation w/ e-Cooling
Chart: 
| 0 | 5 | 5 | 5.5 | 5.5 | 10.5 | 10.5 | 11 | 11 | 16
Strong Cooling | 8.81 | 8.81 | 0 | 0 | 8.81 | 8.81 | 0 | 0 | 8.81 | 8.81
Weak Cooling | 3.03 | 3.03 | 0 | 0 | 3.03 | 3.03 | 0 | 0 | 3.03 | 3.03
Dump and refill
Store ~8 hours
JLEIC for QCD Frontier
Accumulation from linac
Stacking/Pre-cool
Emittance preservation
Emittance preservation
150 MeV
8 GeV
Up to 200 GeV
DC cooler
4.3 MeV
BB cooling
ERL cooler
Up to 109 MeV
collider Ring
High Energy Booster
proton
Low Energy Booster
~20 GeV
Pre-bunch splitting
bunch splitting
12.1 GeV
Accumulation from linac
Phase painting
Pre-cool
BB cooling
41 MeV/u
4.3 GeV
Up to 78 GeV/u
DC cooler
ERL cooler
Up to 43 MeV
collider Ring
Low Energy booster
Stacking, emittance preservation
2.08 GeV
DC cooler
1.1 MeV
Lead ion
DC cooler
Pre-bunch splitting
High Energy booster
Bunch splitting
~20 GeV
emittance preservation
Ring | Functions | Kinetic energy (GeV / MeV) |  |  | Cooler type
 |  | Proton | Lead ion | Electron | 
Low Energy Booster | Accumulation of positive ions |  | 0.1 (injection) | 0.054 | DC
High Energy booster | Maintain emitt. during stacking | 7.9 (injection) | 2 (injection) | 4.3 (proton) 1.1 (lead) | DC
 | Pre-cooling for emitt. reduction | 7.9 (injection) | 7.9 (ramp to) | 4.3 | DC
collider ring | Maintain emitt. during collision | Up to 100 | Up to 40 | Up to 54.5 | ERL
ERL-Circulator Cooler: Critical R&D
Design specs: 1.5 A, 3.2 nC, 225 MW CW, 476 MHz
Technology: magnetized source, ERL, circulator ring
Good performance for up to 150 GeV for p, heavy ions
Circulator cooler ring
ERL ring
Optimization 4: Full Size HE Booster
Beam formation time (including detector turn-around) affects average (integrated) luminosity
The high energy booster is same size of the collider ring
A new beam is made while another one is in collision
The effective beam formation time is reduced to ~5 min from 30 min normal beam formation time
Optimization of JLEIC Integrated Luminosity Without On-Energy Cooling*
High luminosity ~1033-34/cm2/s
High polarization > 80%
Full acceptance detection
DC e-Cooler: Matured Technology
IMP
Fermilab
COSY
Chart: 
| 5 | 10 | 15 | 20 | 25 | 30
 | 10.9477 | 10.1657 | 9.488 | 8.895 | 8.3718 | 7.9067
beam store: 60 min
One beam in collision
A new beam is being formed
Optimization 5: Beam-Beam Leveling
Beam-beam parameters are true beam physics limit
When proton emittance degrades, spot sizes of both electron and proton beam increases, leading to decrease of beam-beam parameters
This provides opportunity to increase electron current (top-off by a full energy injector) to boost proton beam-beam parameter
Chart: 
| 5 | 20 | 35 | 50 | 65
x-dir | 0.015 | 0.008 | 0.006 | 0.005 | 0.004
y-dir | 0.0056 | 0.0043 | 0.0037 | 0.0034 | 0.0032
x-dir, leveling | 0.015 | 0.015 | 0.015 | 0.014 | 0.012
y-dir, leveling | 0.0056 | 0.0079 | 0.0091 | 0.0094 | 0.0088
Chart: 
| 5 | 20 | 35 | 50 | 65
No leveling | 1.3 | 1.3 | 1.3 | 1.3 | 1.3
Leveling | 1.3 | 2.4 | 3.2 | 3.6 | 3.6
Chart: 
| 5 | 20 | 35 | 50 | 65
No leveling | 7.57 | 5.45 | 4.62 | 4.15 | 3.84
With leveling | 7.57 | 10.07 | 11.37 | 11.5 | 10.62
Average luminosity: 4.6 9.7
JLEIC Luminosity Performance
Chart: 
| 21.9 | 31.6 | 44.7 | 63.3 | 80 | 89.4 | 98
preCDR-100 | 2.28 | 4.88 | 10.54 | 7.96 | 4.8 | 1.87 | 0.743
140 GeV CM upgrade | 2.28 | 4.88 | 10.6 | 8.6 | 9.339 | 6.356 | 2.42 | 0.921
With ERL cooling
Chart: 
| 21.9 | 31.6 | 40 | 44.7 | 49 | 52.9 | 54.8 | 56.6 | 63.3 | 69.3
Proton 100 GeV | 2.28 | 4.88 | 11.4 | 10.54 | 8.24 | 5.51 | 3.69 | 2.49 | 0.65 | 0.22
Proton 150 GeV | 3.07 | 3 | 2.35 | 2.1 | 1.2 | 0.31 | 0.11
Proton 200 GeV, no cooling | 6.17 | 8.21 | 8.6 | 8.09 | 4.8 | 1.87 | 0.743
Proton 300 GeV, no cooling | 3.48 | 7.35 | 9.05 | 5.4 | 1.8 | 0.792
proton 400 GeV, no cooling | 8 | 9.34 | 10.26 | 6.36 | 2.42 | 0.921
Average luminosity was calculated assuming
2 hr. proton store with high energy bunched beam electron cooling
1 hr. proton store without high energy bunched beam electron cooling
5 min beam formation time (mainly due to detector overhead)
75% duty factor of machine operation.
Emittance Evolution If No Cooling
Optimization 6: Unmatched Beam Spot Size at IP
In strong beam-beam region, matching beam spot sizes is a must in order to mitigate this nonlinear effect. Such requirement can be relaxed in weak beam-beam region
Smaller beam spot size could boost luminosity
Chart: 
| 5 | 20 | 35 | 50 | 65
Beam spot matched | 1.31 | 1.2 | 1.08 | 0.9 | 0.78
Beam size not matched | 1.51 | 1.27 | 1.14 | 1.06 | 0.98
Average luminosity: 1 1.1
Optimization 3: Reduction of Bunch Repetition Rate
Ion bunch charge is limited by high energy electron cooling (electron bunch charge due to e-gun and transport in ERL/circulator ring)
If no such cooling, bunch repetition rate can be reduced
Smaller repetition rate boosts luminosity L ~ Ie Ip / f
* Work supported by U.S. DOE Contract No. DE-AC05-06OR23177
No Cooling in Collision (>150 GeV)
Simulations show cooling driven by an ERL-Circulator Cooler is not effective to suppress IBS at high energy
Such cooler is also high cost and technical challenges
We must consider an operation scenario with no cooling
What really matters is integrated luminosity (average luminosity over machine run)