## Slide 1: IR Magnet Requirements
V.S. Morozov
on behalf of the JLEIC non-linear dynamics and detector study groups
IR Magnet Discussion with Peter McIntyre, JLab
March 14, 2017

## Slide 2
Detector Region Layout
Forward hadron spectrometer
low-Q2 electron detection
and Compton polarimeter
p
(top view in GEANT4)
e
ZDC
IP
e-
ions
ion crab cavities
e- crab cavities
forward ion detection
forward e- detection
Compton polarimetry
dispersion suppressor/
geometric match
spectrometers

## Slide 3: Interaction Region
Ion IR magnets
  Quadrupoles: QFFB3_US, QFFB2_US, QFFB1_US, QFFB1, QFFB2, QFFB3
  Spectrometer dipoles: SB1, SB2
ions
IP
QFFB3_US
QFFB2_US
QFFB1_US
SB1
QFFB1
QFFB2
QFFB3
SB1

## Slide 4: IR Ion Magnet Parameters
Assuming 100 GeV/c
Parameters are determined primarily by detection requirements rather than beam dynamics
Bottom-up study of multipole requirements in progress
Note: parameters are still being fine-tune but no major changes
Name | Type | Length [m] | Good-field radius [cm] | Inner radius [cm] | Outer radius [cm] | Min. beam separation [cm] | Strength [T or T/m] | Pole-tip field [T]
QFFB3_US | Quad [T/m] | 1 | 3 | 4 | 12 | 36.0 | -116 | -4.6
QFFB2_US | Quad [T/m] | 1.5 | 3 | 4 | 12 | 26.5 | 149 | 6
QFFB1_US | Quad [T/m] | 1.2 | 2 | 3 | 10 | 18.0 | -141 | -4.2
SB1 | Dipole [T] | 1.5 | 4 | 17 | 24 | 25.0 | -2 | -1.3
QFFB1 | Quad [T/m] | 1.2 | 4 | 6.8 | 17.1 | 35.9 | -88 | -6
QFFB2 | Quad [T/m] | 2.4 | 4 | 11.8 | 24.7 | 48.2 | 51 | 6
QFFB3 | Quad [T/m] | 1.2 | 4 | 17 | 26.7 | 67.2 | -35 | -6
SB2 | Dipole [T] | 4 | 4 | 40 | 90 | 102 | 4.7 | 4.7

## Slide 5: Interaction Region
Electron IR magnets
  Quadrupoles: QFFB4e, QFFB3e, QFFB2e, QFFB1e, QFFB1e_US, QFFB2e_US, QFFB3e_US
electrons
IP
QFFB4e
QFFB3e
QFFB1e
QFFB1e_US
QFFB2e_US
QFFB3e_US
QFFB2e

## Slide 6: IR Electron Magnet Parameters
Assuming 10 GeV
Parameters are determined primarily by beam size and available space
Multipole tolerance study has not been done yet
One has to consider effect of the solenoid fringe field
Note: parameters are still being fine-tune but no major changes
Name | Type | Length [m] | Good-field radius [cm] | Inner radius [cm] | Outer radius [cm] | Min. beam separation [cm] | Strength [T/m] | Pole-tip field [T]
QFFB4e | Quad | 0.5 | 4 | 5 | 11 | 21 | -3.1 | -0.16
QFFB3e | Quad | 0.58 | 4 | 5 | 11 | 15 | 47.9 | 2.39
QFFB2e | Quad | 0.7 | 2 | 3 | 8 | 10.5 | -57.7 | -1.73
QFFB1e | Quad | 0.4 | 1.2 | 2 | 6 | 8 | 24.4 | 0.49
QFFB1e_US | Quad | 0.7 | 2 | 3 | 7 | 12 | -43.9 | -1.32
QFFB2e_US | Quad | 0.7 | 4 | 5 | 10 | 16 | 45.5 | 2.28
QFFB3e_US | Quad | 0.5 | 4 | 5 | 10 | 22 | -16.4 | -0.82

## Slide 7: Error Issue
  Assume conservative errors, σ of Gaussian distribution
 | Dipole | Quadrupole | Sextupole | BPM (noise)
x displacement(mm) | 0.3 | 0.3, FFQ0.03 | 0.3 | 0.05
y displacement(mm) | 0.3 | 0.3, FFQ0.03 | 0.3 | 0.05
x-y rotation(mrad) | 0.3 | 0.3, FFQ0.05 | 0.3 | -
s displacement(mm) | 0.3 | 0.3, FFQ0.03 | 0.3 | -
Strength error(%) | 0.1 | 0.2, FFQ0.03 | 0.2 | -
Corrections: Orbit Correction, Twiss @ IP, Tune correction, Beta-beat correction, Chromaticity correction, Decoupling.

## Slide 8: Closed Orbit Distortion after Correction
 | ex/ey(nor. mm-mrad) | x/y @ IP | x/y @ FFQ
Case 1, strong cooling | 0.35/0.07 | < 1 σ | < 0.01 σ
Case 2, large emittance | 1.2/1.2 | < 0.6 σ | < 0.006 σ
x/y @ IP didn’t include local orbit correction
Start from IP, 10 seeds

## Slide 9: Dynamic Aperture after Correction
100 GeV proton | ex/ey(nor. mm-mrad) | DA origin | DA with error
Case 1, strong cooling | 0.35/0.07 | ~ 90 σ | ~ 60 σ
Case 2, large emittance | 1.2/1.2 | ~ 48 σ | ~ 32 σ
90 σ
With error & correction
10 seeds
60 σ
With error & correction

## Slide 10: Magnet Quality (FFQ: Bottom-up approach)
Top-down approach by using
LHC FFQ measured data
DA results are OK for 100 GeV proton case.
 | ex/ey(nor.) | DA
Case 1 | 0.35/0.07 | ~ 16 σ
Case 2 | 1.2/1.2 | ~ 10 σ
LHC FFQ

## Slide 11: Magnet Quality (FFQ: Top-down estimation)
Larger beam emittance with week cooling results in the tighter limit multipole
Survey with 0.9/0.9 mm-mrad of emittance gives a balance between multipole field of IR triplet and dynamic aperture.
DA
DA: 10 σ for 60 GeV proton
& 12 σ for 100 GeV proton

## Slide 12: JLEIC Baseline Parameters
CM energy | GeV | 21.9 (low) |  | 44.7 (medium) |  | 63.3 (high) | 
 |  | p | e | p | e | p | e
Beam energy | GeV | 40 | 3 | 100 | 5 | 100 | 10
Collision frequency | MHz | 476 |  | 476 |  | 476/4=119 | 
Particles per bunch | 1010 | 0.98 | 3.7 | 0.98 | 3.7 | 3.9 | 3.7
Beam current | A | 0.75 | 2.8 | 0.75 | 2.8 | 0.75 | 0.71
Polarization | % | 80% | 80% | 80% | 80% | 80% | 75%
Bunch length, RMS | cm | 3 | 1 | 1 | 1 | 2.2 | 1
Norm. emittance, hor / ver | μm | 0.3/0.3 | 24/24 | 0.5/0.1 | 54/10.8 | 0.9/0.18 | 432/86.4
Horizontal & vertical β* | cm | 8/8 | 13.5/13.5 | 6/1.2 | 5.1/1.0 | 10.5/2.1 | 4/0.8
Ver. beam-beam parameter |  | 0.015 | 0.092 | 0.015 | 0.068 | 0.008 | 0.034
Laslett tune-shift |  | 0.06 | 7x10-4 | 0.055 | 6x10-4 | 0.056 | 7x10-5
Detector space, up/down | m | 3.6/7 | 3.2/3 | 3.6/7 | 3.2/3 | 3.6/7 | 3.2/3
Hourglass(HG) reduction |  | 1 |  | 0.87 |  | 0.75 | 
Luminosity/IP, w/HG, 1033 | cm-2s-1 | 2.5 |  | 21.4 |  | 5.9 | 

## Slide 13
Discussion on the layout
0.4 m
0.3 m
0.5 m
0.3 m
0.2 m
1 m
The space for magnet layout seems tight, we need realistic advises from magnet group and mechanic group
Skew quads: 0.1 m; corrector: 0.2 m
Skew quads are just beside the FFQ without space.
: Skew Quadrupole
Notes: 13

## Slide 14
Discussion on the layout
0.4 m
0.3 m
0.5 m
0.9 m
0.9 m
0.3 m
0.2 m
1 m
0.5 m
0.5 m
The space downstream of IR in ion collider ring is also used for ion forward detection, we need discussion with nuclear physics group
downKicker02downSkew01: 0.2 m
: Skew Quadrupole
Notes: 14

## Slide 15
An Compensation Scheme (Skew quads)
Correctors: 0.2 m
ipuscorr1->vkick= -0.0007491948842; -1.2 T;
ipuscorr2->vkick= 0.00182813549; 3.0 T;
ipdscorr1->vkick= 0.0009885706997; 1.6 T;
ipdscorr2->vkick= -0.0004494537749; -0.7 T;
If the field direction of the detector solenoid is reversed, we can reduce the strength of the 4 vertical correctors.
: Skew Quadrupole
Notes: 15

## Slide 16
An Compensation Scheme (Skew quads)
Correctors: 0.2 m
ipuscorr1->vkick= -0.0007491948842; hkick= 2.958152587e-06;
ipuscorr2->vkick= 0.00182813549; hkick= -5.545443962e-06 ;
ipdscorr1->vkick= 0.0009885706997; hkick= 9.391893355e-06 ;
ipdscorr2->vkick= -0.0004494537749; hkick= -3.571220222e-06;
Strengths of horizontal correctors are 2 order lower, so we do not need to worry about that.
: Skew Quadrupole
Notes: 16

## Slide 17
An Compensation Scheme (Skew quads)
Skew quads: 0.1 m
qffus01s->k1s = 0.03902141928 ; qffus02s->k1s = -0.01476904268 ; qffus22s->k1s = -0.02026700407 ; qffus03s->k1s = 0.01908813591 ;
qffds01s->k1s = -0.04199200154 ; qffds02s->k1s = 0.0220116615 ; qffds22s->k1s = 0.01262536581 ; qffds03s->k1s = -0.00742312655 ;
Strengths of those skew quads are reasonable.
: Skew Quadrupole
Notes: 17

## Slide 18
An Compensation Scheme (Skew quads)
Strength changes of those IR triplets are acceptable.
: Skew Quadrupole
 | origin | new | 
qffus01->k1 | -0.42112 | -0.43308 | 2.8%
qffus02->k1 | 0.446485 | 0.44312 | -0.8%
qffus03->k1 | -0.34684 | -0.33007 | -4.8%
qffds01->k1 | -0.26374 | -0.25979 | -1.5%
qffds02->k1 | 0.152085 | 0.154926 | 1.9%
qffds03->k1 | -0.10586 | -0.11682 | 10.3%
Notes: 18

## Slide 19: Next Steps
Implement the smaller baseline
Reevaluate IR quad multipole requirements using reduced quad apertures
Consider locations of multipole corrector spools
Simulate local compensation of systematic multipoles
Estimate random multipoles
Consider space for skew quads and correctors for detector solenoid compensation