## Slide 1: JLEIC Impedance Summary
Rui Li
JLEIC Impedance Meeting
3-25-2019

## Slide 2: Outline
Broadband impedance
  Scaling from existing machine
  Major contributors
  Other ion machine impedances
  Roman Pot
Narrowband impedance

## Slide 3: Broadband Impedance in JLEIC
Impedance budget studies
  Complete inventory of impedance-generating components
  Engineering design and drawing of each components
  EM field modeling for wakefield or impedance spectrum
Current status of impedance studies in JLEIC
  Engineering design is in its early phase
  Component counts are done (subject to modification)
  Impedance are estimated using impedance budget of
  existing machines for reference

## Slide 4: Broadband Impedance Estimation: JLEIC e-Ring
Component Counts
Elements | e-Ring
Flanges (pairs) BPMs Vacuum ports Bellows Vacuum Valves Tapers Collimators DIP screen slots Crab cavities RF cavities RF valves Feedback kickers IR chamber | 1215 405 480 480 23 6 16 470 2 32 68 2 1
(T. Michalski)
Impedance Estimation
Broadband Impedance | Reference: PEP-II | Reference: SUPERKEKB
 | 99.2 | 28.6
 | 0.09 | 0.02
 | 7.7 | 19
 | 60 | 13
JLEIC plans to use PEP-II vacuum systems
Effective impedance is bunch length
dependent
(K. Deitrick)

## Slide 5: Electron Ring Breakdown (using PEPII elements)
L/L_tot
15%
22%
25%
30%

## Slide 6: Broadband Impedance Estimation: JLEIC ion-Ring
Component Counts
Elements | p-Ring
Flanges (pairs) BPMs Vacuum ports Bellows Vacuum Valves Tapers Collimators DIP screen slots Crab cavities RF cavities RF cavity bellows RF valves Feedback kickers Roman Pot IR chamber | 234 214 92 559 14 6 16 - 8 40 40 24 2 2 1
(T. Michalski)
Impedance Estimation
Broadband Impedance | Reference: PEP-II
 | 97.6
 | 0.08
 | 8.6
 | 80
(K. Deitrick)
The short bunch length (1.0cm) at
collision is unprecedented for the ion
beams in existing ion rings
Bunch length varies through the whole
bunch formation process

## Slide 7: Broadband Impedance for Other Lepton Rings

## Slide 8: Broadband Impedance for Other Ion Rings
RHIC (measurement)
  (“Longitudianl Impedance of RHIC”, M. Blaskwicz, etc)
  (“Transverse Impedance Measurement in RHIC and the AGS”,
  N. Biancacci, etc)
LHC (measurement)
  (“Beam Measurement of LHC Impedance…”, J. F. E. Muller, etc)

## Slide 9: Roman Pot
The Roman Pot is an experimental technique for the detection of forward protons from elastic or diffractive scattering.
It has been successfully employed in other machines like the SPS, TEVATRON, RHIC and DESY.
The challenging constraints of LHC, such as the narrow high intensity beam with energy of 7 TeV, the Ultra High Vacuum and the high radiation fluxes have required the development of new Roman Pots.
measured value for (Z_long/n)eff LHC= 90mΩ

## Slide 10: Roman Pot

## Slide 11: Narrowband Impedance in JLEIC
RF Cavities
  PEPII RF cavities
  Ion ring cavities
  Crab cavities
Other Components
  IR vacuum chamber
  Collimators
  IR Bellows
  Roman Pot

## Slide 12: Narrowband Impedance: JLEIC e-Ring RF Cavity
RF cavity in e-Ring (PEP-II cavities)

## Slide 13: Narrowband Impedance: Ion-Ring RF Cavity
956 MHz 2-cell Cavity
as tradeoff between accelerating
and HOM-damping efficiency
causes LCBI
(F. Marhauser)

## Slide 14: Narrowband Impedance: Ion-Ring RF Cavity
956 MHz 2-cell Cavity
waveguide couplers
reduced LCBI growth rate
(F. Marhauser)

## Slide 15: Narrowband Impedance: Crab Cavity
Prototype converging to a 952.6 MHz 2-cell RFD cavity.
Bare cavity impedance
Damping under study
Chart: Frequency [MHz]
Eigen-X | 2.566 | 141.2833 | 3.5531 | 13.0334 | 2.3909e-06 | 24.4583 | 0.94071 | 5.6682e-06 | 17.1179 | 4.3619 | 0.69041 | 4.3246 | 0.013377 | 0.3637 | 2.4001 | 0.087282 | 0.19186 | 0.70457
Eigen-Y | 2.1988 | 6.0823 | 4.7844 | 28.038 | 1.0611 | 1.6791 | 6.4409 | 7.9323e-06 | 2.9563 | 0.027475 | 3.0913 | 2.1878e-05 | 2.7541e-05 | 0.10919 | 0.11189 | 1.1049 | 3.4246e-06 | 0.076496 | 0.36503 | 5.9499e-06
Chart: Frequency [MHz]
Eigen-Z | 81.3102 | 130.4091 | 33.958 | 0.86543 | 0 | 2.523 | 0.39059 | 1.4737 | 2.147 | 1.248 | 5.008 | 3.9856e-06 | 2.3327 | 0.077005 | 4.4513e-06 | 0.19095 | 0.038752 | 2.5505e-05 | 1.3035 | 3.7942
2 hook couplers
2 wave guides
(HK Park)

## Slide 16: Narrowband Impedance: IR Chamber
JLEIC IR Chamber CAD Model
(Marhauser)

## Slide 17
New IR Chamber Design Underway

## Slide 18: Narrowband Impedance: Roman Pot
*For LHC, the dark area is beyond bunch frequency range (bunch rms length=7cm)
*For JLEIC, the dark area still contributes

## Slide 19
Collimator
Ongoing Design of Other Components
Shielded IR Bellow

## Slide 20: Summary of JLEIC Impedance Status
We are at the beginning phase of impedance studies
Preliminary estimations are done
Engineering design and EM modeling are underway