## Slide 1: C100 gradient recovery effort
Anna Solopova
5-3-2018

## Slide 2: Outline
Progress to date
Waveforms!
Limitations and mysteries
Plans

## Slide 3: Gradient push progress
Started on March 23
South up 18.6MeV/m from 2017
  gradient was just sitting there, sad and forgotten
North down 10.5MeV/m from 2017
  cryo events, vacuum, FE
MeV/m | Total | North | South
March 2017 | 933.5 | 423.6 | 424.2
March 2018 | 860.1 | 390.8 | 384.9
May 2018 | 940.5 | 413.2 | 442.8
North is up 22.4 MeV/m from the start
South is up 58 MeV/m
Chart: 
| 0L04 | 1L22 | 1L23 | 1L24 | 1L25 | 1L26 | 2L22 | 2L23 | 2L24 | 2L25 | 2L26
3/1/2017 | 85.673 | 95.06 | 95.774 | 90.909 | 65.744 | 76.146 | 84.952 | 85.617 | 82.271 | 84.021 | 87.304
3/22/2018 | 84.385 | 75.019 | 73.794 | 79.114 | 77.238 | 85.589 | 73.85 | 77.91 | 73.43 | 84.35 | 75.39
May-18 | 84.399 | 81.2 | 71.995 | 79.24 | 87.57 | 93.17 | 91.49 | 83.02 | 83.3 | 90.44 | 94.5
Energy reach: NL 1079MeV; SL 1080MeV

## Slide 4: Trips
Trips: things get worse before they get better.
  Total RF trip rate now is the same as in March 2017
  C100 trip rate is 0.1/hr lower

## Slide 5: Waveforms
Allow to investigate each trip at higher resolution than archiver
Show events when a cavity caused others to trip, but stayed on
  Helps keep the gradient up in “innocent” cavities.
Possible to create patterns for each type or trips
  Automation of the gradient recovery process in the future

## Slide 6: Waveforms
CFQE2
CRFP
CRFPP
CRRP
CRRPP
DETA2
DFQES
GASK
GLDE
GMES
IASK
IMES
OpsSummary1
PASK
PLDE
PMES
QASK
QMES
Viewer page Available from JMenu – System Expert - RF

## Slide 7: Waveforms
Started with 2L25 and 5 signals per cavity per trip on 4-10-18
17 waveforms are collected from all C100 cavities on each trip starting 4-24-18
IOC time sync and harvester flag issues
  Not all files are saved for each trip
  Work is ongoing
  If we have 30% of trips, we are still good
Version 2 web viewer and Tom’s LabView viewer for analysis
OPS are already using it

## Slide 8: Limitations and mysteries
Quiet times vs trips at the same gradient for no good reason
  Can it be solved through WFS?
Microphonics-induced trips
Klystrons not providing 10kW: cavity runs out of power and trips
  To be addressed this summer through optimization and maybe klystron swaps
Quench vs some other fault resolution
Electrical noise and single-point event filtering
  Recent storm left SL C100 off for an hour, still ringing 3 hours later that night.

## Slide 9: Suddenly, trips! Hundreds of them!
Beginning of April: same gradient, stable for days. No obvious changes associated with instability. Frequent trips.
Now: redistributed gradient, reduced 2MeV – stable.
Popped a field emitter on cavity 6, lost 1MeV on May 2.
1L24 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | Total
GSET April 7 | 0 | 16 | 18 | 17 | 18 | 17 | 16 | 14 | 116
GSET May 3 | 0 | 16 | 17.2 | 17.5 | 17.5 | 16 | 15.5 | 13.5 | 113.2

## Slide 10: 1L25-3 TDOFF
1L25-3 POFF was optimized following a “violent quench event” event on April 26, when cavity 4 quenched and LL went over 96%. Tom will elaborate.
TDOFF shifted ~40 degrees, leaving cavity off tune.
Manually tuned a day later, then it was optimized and off tune again
  Ops followed the optimization procedure which works well on all other cavities.
Cavity was running at 19MeV all this time, tripping more often after wrong TDOFF.
May 2 owl shift it was bypassed due to repeated trips and SOS-ing, recovered next day to only 15.5MeV
Swapped FCC and an attenuator, checked cable connections – no luck
Elog references 3569764 3570893 3570260

## Slide 11: Klystron power limits
Typical event: 2L25 Cavity 4 ran out of power at 6kW multiple times.
22 klystrons trip at CRFP below 10kW. 46 are not not linear above 10kW (spec is 10.5)
Courtesy of T. Powers

## Slide 12: Single point events
2L22 electrical noise from the storm on April 25

## Slide 13: Plans in an ideal world
Trip data analysis
  Patterns
  Normal decay times from planned RF off
  “Window of normality” for certain signals
  Automation: run trip analyzer on the background, alert ops “this cavity was unstable first X% of trips”
More powerful and flexible WFS viewer
Klystron optimization and swap
Phase lock – cut recovery time to ~30 seconds
Filter single point events?
Work with OPS to be mindful of the gradient
  C100 recovery procedures and other tools

## Slide 14: Tools for the OPS
C100 POFF optimization guidance
Cavity history tool files an OPS-PR for ODVH change
  Pop-up reminder if the reason for derating was “Beam instability”
Arc detector fault notification on the Wall
AutoRecovery script requires operator intervention on arc test fault and repeated quench faults over a short period of time
Automatic TDOFF adjustment based on CRFP/DETA2 fit

## Slide 15: Thanks to the team:
Clyde Mounts
Ramakrishna Bachimanchi
Tom Powers
George Lahti
Adam Carpenter
Chris Slominski
Theo Larrieu
OPS